## Slide 1: Machine Availability and Reliability in CEBAF
A presentation to the Tesla Technology Collaboration (TTC) meeting; Aomori, Japan
Michael D McCaughan
SRF Operations
At Thomas Jefferson National Laboratory
Thomas Jefferson National Acceleration Facility
CEBAF Particle Accelerator

## Slide 2: Scheduling
M. McCaughan
TTC: Aomori, Japan 12Oct22
Experiments are proposed annually to a panel of outside experts [The Program Advisory Committee or PAC] and are ranked according to their scientific merit and awarded some number of experiment day.
PAC Days x 2 = Scheduled Days
(Stuff happens…)
This accounts for projected inefficiencies and failures, but not experimental overhead. (Say installing a new spectrometer…)
Experiments are arranged into a schedule with combined input of members of scheduling committee (Experimental Hall leaders, Physics & Accelerator Division leaders, Director of Accelerator Operations, etc.):
www.jlab.org/physics/experiments/schedule

## Slide 3: Scheduling (Cont.)
M. McCaughan
TTC: Aomori, Japan 12Oct22
Implicit in this schedule are certain negotiated activities which are overhead:
Beam Studies + RF Recovery (12 hrs/week)
Maintenance (4 hr/week)
(S)RF Maintenance (8 hrs/week)
Beam Tuning (8 hrs/week) [Program reconfiguration, quality issues, restore beam after one of the above… etc.]
This time is all taken out of that ‘inefficiency’ time granted by PAC; the remaining time: 136 hrs/week are scheduled research.
Now as noted – stuff happens – so if beam stops for longer than 5 minutes for a reason other than the scheduled program this is considered a Down Time. These down times are created and managed by the operations crew on-duty, but may later revisited offline by the operability group with the advantage of hindsight to make sure binning/categorization is appropriate for affected systems once the situation is clear.

## Slide 4: Downtime: Example
M. McCaughan
TTC: Aomori, Japan 12Oct22

## Slide 5: Downtime Example
M. McCaughan
TTC: Aomori, Japan 12Oct22
Data is sliced up lots of different ways other than time accounting for machine reliability purposes.
(Outside scope of this talk)
Details available upon request…

## Slide 6: Beam Time Accounting
M. McCaughan
TTC: Aomori, Japan 12Oct22
Recorded online; checked by Crew Chief.
Hall states:
Up – Executing program
Tune – Tuning beam for program
BNR – Beam Not Requested (Accelerator okay; hall unready)
Down – No beam from Accelerator
Off – Not scheduled for beam
CEBAF States:
BS – Beam Studies
Restore – Scheduled machine set-up time at start of run / after long downs
ACC – Accelerator configuration change
Down – No beam available
SAD – Scheduled Accelerator Down [Off]
States != OFF / SAD count against budgeted PAC hours

## Slide 7: Reliability
M. McCaughan
TTC: Aomori, Japan 12Oct22
Research
Research = Physics Uptime (BTM) + Quality – Physics Down
Quality – scheduled extra hours for sub-optimal setups due to experiment multiplicity (ex. Low polarization, energy, current, etc. means running longer to achieve the same data set)
Physics Down = Recorded Downtimes – Hall down/unavailable
Tune and Restore time:
Tune/Restore Time = Accelerator Configuration Change + Restore
Note recovery periods from downtimes are encapsulated in the downtimes and will not be extracted unless excessive (O(days+))
Total Beam Delivered & Scheduled:
Total Delivered = Research + Tune/Restore + Beam Studies
Total Scheduled = Total Delivered + Down Times – Agreed Maintenance
Reliability == Total Delivered / Total Scheduled
(Note: Further corrective action to this number may be taken for other unaccounted for items like integrated FSD faults time, schedule / program changes/etc.) The number following these 2nd order corrections is what is submitted with Joule report.

## Slide 8: Reliability
FY21 reliability (short run after long shutdown): Achieved 775.9 total delivered hours/780 planned [1104 scheduled] 70.3% reliability
FY22 reliability: (33 weeks (1 technical stop, 2 recovery, 30 physics) @ 3 linac energies (910, 980, 1047 MeV/linac)) Achieved 4153 delivered operating hours & 1293 unscheduled failure hours; reliability 76%
FY22 weekly reliability
FY21 weekly reliability
Transition to higher energy after FY22 SAD has been painful
CEBAF Reliability (performance measure reported to DOE)
FY21 weekly reliability
Availability/Reliability in CEBAF
M. McCaughan
TTC: Aomori, Japan 12Oct22
CEBAF Target: 80% / year

## Slide 9
Michael McCaughan
-Fin-
12000 Jefferson Ave. Suite 19
Newport News, VA 23606 USA
O: (757) 269-5572 / michaelm@jlab.org

## Slide 10: Back-Up Slides
Availability/Reliability in CEBAF
M. McCaughan
TTC: Aomori, Japan 12Oct22

## Slide 11: Back-Up Slides
Availability/Reliability in CEBAF
M. McCaughan
TTC: Aomori, Japan 12Oct22