## Slide 1
Younguk Sohn
Pohang Accelerator Lab., POSTECH
Oct 11-14, 2022
Machine Availability and Reliability of PLS-II at PAL
TTC2022 Aomori, TESLA Technology Collaboration

## Slide 2: Abstract
3 SRF cryomodules have been operated since September, 2012 for the Pohang Light Source (PLS-II). They are the CESR-B type which were fabricated by the industry with the turn-key contract. For the less faults, the operation Vacc and RF power are about 60-70% of their specifications. There have been no severe problem in the coupler/window and cavity itself. But recently two vacuum leak events between cavity and He vessel were found, after 7.6 years’ and 7 years’ operation. Also at the beginning several years, we were suffered from the turbine troubles of He refrigerators.
The fault statistics and analysis of SRF system at PLS-II are reported in the presentation

## Slide 3: Parameters of PLS-II RF System
Parameters | Value
Energy [GeV] | 3
Current [mA] | 400
Emittance [nm-rad] | 5.9
Beam loss power by synchrotron radiation [kW] | 500
RF frequency [MHz] | 499.973
No. of RF cavities | 3
Accelerating voltage, Vacc [MV] | 4.5
Vacc / cavity, [MV] | 1.5
Klystron amplifier | 3- 300 kW amp.
Cryogenic cooling capacity @4.5 K [W] | 700

## Slide 4: Accelerating Voltages @ Bare Cavity
2.0 MV = 6.7 MV/m
2.8 MV = 9.3 MV/m
1.4 MV = 4.7 MV/m
(CESR-B cavities, operation voltage: 1.4 MV (4.7 MV/m)

## Slide 5: SRF Modules @Tunnel
SRF module 2
SRF module 3

## Slide 6: Operation Parameters
RF voltage, per unit: 1.4 MV (4.7 MV/m)
Forward power through window (coupler), per unit: 140 ~ 190 kW CW
Reflected power, per unit: < ~2 kW
Vacuum pressure at window and cavity: ~ middle 10-10 mbar

## Slide 7: Operation Carrier of Each Module
Year |  | Y-2012 |  | Y-2013 |  | Y-2014 |  | Y2015 |  | Y2016 |  | Y-2017 |  | Y2018 |  | Y2019 |  | Y-2020 |  | Y2021 |  | Y2022 | 
Status |  | 1st | 2nd | 1st | 2nd | 1st | 2nd | 1st | 2nd | 1st | 2nd | 1st | 2nd | 1st | 2nd | 1st | 2nd | 1st | 2nd | 1st | 2nd | 1st | 2nd
CM1 | Installation & commissioning |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Operation |  |  |  |  |  |  | 8 years and 7 months |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Out of service |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CM2 | Installation & commissioning |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Operation |  |  | 9 years and 9 months |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Out of service |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CM3 | Installation & commissioning |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Operation |  | 7 years |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Out of service |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 years & 4 months |  |  |  |  |  | 
Warmed up to room temperature every years for maintenance of refrigerator
For some years, un-planed warmed up by many reasons such as site blackouts, cryogenic problems, site utility maintenances, …
Partial warmed up to 40K at beginning of each user-service term for vacuum improvement during the first 6 months operation after installation
Regular partial warmup for every 5 user-services
Vacuum leakage He vessel to cavity during cooldown

## Slide 8: History of Partial Warmup (Feb.-Jul, 2013)
Partial warming-up cavity up to 40K
Threshold pressure vacuum bursts >1 x 109 mbar

## Slide 9: Partial Warmup & Cooldown Mass-Spectrometer (RGA)
4 days before partial warmup, and 3 days after re-cooldown
Before partial warmup
After re-cooldown
Partial warmup
Partial Pressure of Hydrogen (Black)

## Slide 10: Partial Warmup & Cooldown
During partial warmup & cooldown with TMP operation
Ion pump off
(00:28)
TMP on
1.4e-8 mbar
(01:00)
1 Ion pump @window on by mistake
(03:40)
H: Mass 2
N2: Mass 28
O:Mass 16
N:Mass 14
C, Mass 12
All Ion pump on
TMP off
Cavity top:43K
Cavity bottom: 31K
(06:07), 2.9e-9 mbar

## Slide 11: Number of SRF fault, SRF fault time
2 modules
3 modules
2 modules
※ SRF includes all components of RF system such as cryomodule, cryogenics, HPRF, LLRF and control

## Slide 12: Number of SRF fault, SRF fault time
2 modules
3 modules
2 modules

## Slide 13: MTBF, MTTR from SRF System only
2 modules
3 modules
2 modules
MTBF: mean time between failures, MTTR: mean time to repair

## Slide 14: Faults for each RF Components
Absorber is the device installed in the coldbox of He refrigeration to remove impure gas from He gas. During absorber A working with every 12 days operation, the valves and vacuum pump manipulation makes He pressure disturbance at the high pressure line of cold box. It occasionally disturbs He pressure of module He vessel.
Pickup is the field pickup probe: with 5~8 user-service terms, condensed gases are expended abruptly then it makes vacuum pressure disturbance at CM3 only.
TL is the power transmission line including water load, circulator and RF switch.
CG is the He refrigerator including compressor, coldbox and He dewar

## Slide 15: Severe Faults, Experienced
Blocking particle filter in LHe supply line during the 1st trying to cooldown cryomodules
Stoppage of expansion turbine in cold box during cavity cooling after planed maintenance: 26 Jan., 2014 (20 days’ out of service), 14 Feb, and 24 Mar., 2017(45 days out of service) maybe impurity makes turbine jamming, but unknow cause and no pre-detected symptoms by system monitoring.
Tearing out of LN2 supply tube (bellows) of MCTL during cavity cooling: 19 Feb. - Mar. 26, 2014 (28 days’ loss of beamtime), mis-design of section bellows and mis-selection of bellow type (blade guide)
Vacuum leakage between He vessel and cavity: CM3 – Sep. 2029, CM1 – Sep. 2022, maybe fatigue of indium sealing through the frequent thermal cycle and aging, resulted to reduced beam current, ordered spare module.
(more than 2 weeks downtime)

## Slide 16: Turbine Troubles
Deformed
Scratch
Contact marks between turbine wheel and exhaust turbine diffuser

## Slide 17: Damaged Bellows
Teared bellows @ MCTL Section 8
LN2 thermal shield
Deformed bellows @ MCTL Section 6
End type of bellow
Guide blade

## Slide 18: Repair of LN2 Lines
VB 3
VB 2
VB 1
Bellow replacement
Improvement of bellow position
& window area
Checking bellows soundness
Improvement of bellow position
& window area
Cutting MCTL vacuum vessel
(10 vacuum ports)
Section 10
Section 9
Section 8
Section 7
Section 6
Section 5
Section 4
※ VB: Valve box for SRF cryomodule
Bellow position is 560mm different than drawing

## Slide 19: Blocking Particle Filter in LHe Supply Line
VB3
VB2
VB1
Filter
Cryomodule
LHe supplying line in MCTL
Line filter

## Slide 20: Discussion
How frequently a cold box and compressor should be maintained for the keep their performance ?
Whether the skipping some procedures (sequences) to resume coldbox operation would be recommended, after safe stop of turbine (just few minutes ~ few hours) due to the facility troubles such as site blackout, losses of cooling water and pneumatic air ?
Is it possible for a large volume of LHe dewar to keep cavity cold (not over 50K) for the long idle standby, ? and recommendable ?
Is there any special idea to detect the possibility of turbine stoppage ?
(We monitor turbine speeds, pressure disturbances around turbines and He impurity of several positions of warm and cold parts)
Life time of ceramic window ?
Calibration of field pickup, how frequently ?
Necessity of dual refrigerators, worthwhile ?
END